## Slide 1: CONTROL UNIT

## Slide 2
The Control Unit was historically defined as one distinct part of the 1946
reference model of Von Neumann architecture.
The function of control unit is to generate relevant timing and control signals to all operations in the computer.
Control Unit is “the brain within the brain”.
It controls the flow of data between the processor and memory and peripherals.
The examples of devices that require a control unit are CPUs and graphics processing units (GPUs).

## Slide 3: FUNCTIONS
The control unit directs the entire computer system to carry out stored
program instructions.
The control unit must communicate with both the arithmetic logic unit (ALU) and main memory.
The control unit instructs the arithmetic logic unit that which logical or
arithmetic operation is to be performed.
The control unit co-ordinates the activities of the other two units as well as all peripherals and auxiliary storage devices linked to the computer.

## Slide 4: TYPES
Control unit generates control signals using one of the two
organizations :
Hardwired Control Unit.
Micro-programmed Control Unit.

## Slide 5: Hardwired Control Unit
Hardwired control units are implemented through use of sequential
logic units or circuits like gates , fliflops , decoders in hardware.
Hardwired control units are generally faster than micro-programmed designs.
This architecture is preferred in reduced instruction set computers (RISC)
as they use a simpler instruction set.
The hardwired approach has become less popular as computers have evolved as at one time, control units for CPUs were ad-hoc logic, and they were difficult to design.

## Slide 6: ADVANTAGES
Hardwired Control Unit is fast because control signals are generated by
combinational circuits.
The delay in generation of control signals depends upon the number of gates.
The performances is high as compared to micro-programmed control unit.

## Slide 7: DISADVANTAGES
The control signals required by the CPU will be more complex
Modifications in control signal are very difficult. That means it requires rearranging of wires in the hardware circuit.
It is difficult to correct mistake in original design or adding new features
in existing design of control unit.

## Slide 8: CONSIST OF:
Control unit consist of a:
Instruction Register
Number of Control Logic Gates,
Two Decoders
4-bit Sequence Counter

## Slide 9: ARCHITECTURE

## Slide 10
An instruction read from memory is placed in the instruction register (IR).
The instruction register is divided into three parts: the I bit, operation code, and address part.
First 12-bits (0-11) to specify an address, next 3-bits specify the operation code (opcode) field of the instruction and last left most bit specify the addressing mode I.
I = 0 for direct address
I = 1 for indirect address

## Slide 11
First 12-bits (0-11) are applied to the control logic gates.
The operation code bits (12 – 14) are decoded with a 3 x 8 decoder.
The eight outputs ( D0 through D7) from a decoder goes to the control logic gates to perform specific operation.
Last bit 15 is transferred to a I flip-flop designated by symbol I.

## Slide 12
The 4-bit sequence counter SC can count in binary from 0 through 15.
The counter output is decoded into 16 timing pulses T0 through T15.
The sequence counter can be incremented by INR.
input or clear by CLR input synchronously.

## Slide 13: EXAMPLE
Consider the case where SC is incremented to provide timing signalsT0, T1, T 2 , T3, and T4 in sequence. At time T4 , SC is cleared to 0 if decoder output D3 is active. This is expressed symbolically by the statement:
D3 T4 : SC ← 0
The timing diagram shows the time relationship of the control signals.

## Slide 14: TIMING DIAGRAM

## Slide 15: MICRO-PROGRAMMED CONTROL UNIT
The idea of microprogramming was introduced by Maurice Wilkes in 1951.
Micro-programs were organized as a sequence of microinstructions and stored in special control memory.
The main advantage of the micro-program control unit is the simplicity of its structure.
Outputs of the controller are organized in microinstructions and they can be easily replaced

## Slide 16
A micro-programmed control unit is implemented using programming approach. A sequence of micro operations are carried out by executing a program consisting of micro-instructions.
Micro-program, consisting of micro-instructions is stored in the control memory of the control unit.
Execution of a micro-instruction is responsible for generation of a set of control signals.

## Slide 17
Micro-Programs: Microprogramming is the concept for generating control signals using programs. These programs are called micro - programs.
Micro-Instructions: The instructions that make micro-program are called micro-instructions.
Micro-Code: Micro-program is a group of microinstructions. The micro- program can also be termed as micro-code.
Control Memory: Micro-programs are stored in the read only memory (ROM). That memory is called control memory.

## Slide 18: ADVANTAGES
The design of micro-program control unit is less complex because micro-
programs are implemented using software routines.
The micro-programmed control unit is more flexible because design modifications, correction and enhancement is easily possible.
The new or modified instruction set of CPU can be easily implemented by
simply rewriting or modifying the contents of control memory.
The fault can be easily diagnosed in the micro-program control unit using diagnostics tools by maintaining the contents of flags, registers and counters.

## Slide 19: DISADVANTAGES
The micro-program control unit is slower than hardwired control unit.
That means to execute an instruction in micro-program control unit requires more time.
The micro-program control unit is expensive than hardwired control unit
in case of limited hardware resources.
The design duration of micro-program control unit is more than hardwired control unit for smaller CPU.

## Slide 20: CONSIST OF :
Control unit consist of a :
Next address generator
Control address register
Control memory
Control data register

## Slide 21: ARCHITECTURE
The address of micro-instruction that is to be executed is stored in the
control address register (CAR).
Micro-instruction corresponding to the address stored in CAR is fetched from control memory and is stored in the control data register (CDR).
This micro-instruction contains control word to execute one or more
micro-operations.
After the execution of all micro-operations of micro-instruction, the address of next micro-instruction is located.

## Slide 23
COMPARISON BETWEEN HARDWIRED AND MICROPRGRAMMED
CONTROL UNIT
ATTRIBUTE | HARDWIRED CONTROL UNIT | MICRO-PROGRAMMED CONTROL UNIT
SPEED | FAST | SLOW
COST OF IMPLEMENTATION | MORE | CHEAPER
FLEXIBILITY | NOT FLEXIBLE, DIFFICULT TO MODIFY FOR NEW INSTRUCTION | FLEXIBLE, NEW INSTRUCTIONS CAN BE ADDED
ABILITY TO HANDLE COMPLEX INSTRUCTION | DIFFICULT | EASIER
DECODING | COMPLEX | EASY
APPLICATION | RISC MICROPROCESSOR | CISC MICROPROCESSOR
INSTRUCTION SET SIZE | SMALL | LARGE
CONTROL MEMORY | ABSENT | PRESENT
CHIP AREA REQUIRED | LESS | MORE 23

## Slide 24: PIPELINING
Pipelining is a technique of decomposing a sequential process into sub-operations, with each sub-process being executed in a segment that operates concurrently with all other segment.

## Slide 25: Example for Pipeline Processing

## Slide 26: Operations in each pipeline stage

## Slide 27: General Four-Segment Pipeline

## Slide 28: Pipeline Speedup

## Slide 29
Q1. In certain scientific computation it is necessary to perform the arithmetic operation (Ai+Bi)*(Ci*Di)
Specify the pipeline configuration to carry out this task.
List the content of all registers of all the registers in the pipeline for i=1 to 6.
Q2. Draw a space time diagram for a six-segment pipeline showing the time it takes to process eight tasks.
Q3. A non-pipelined system takes 50ns to process a task. The same task can be processed in a six-segment pipeline with a clock cycle of 10ns. Determine the speedup ratio of the pipeline for 100 tasks.

## Slide 33: Computer Instructions
The basic computer has three instruction code formats.
Each format has 16 bits.
The operation code(op-code) part of the instruction contains three bits and the meaning of remaining 13 bits depends upon the op-code encountered.

## Slide 34: Computer Instruction Set

## Slide 35: Instruction Cycle
The program is executed in the computer by going thru a cycle for each instruction.
In basic computer, each instruction cycle consists of the following phases:
Fetch an instruction from memory.
Decode the instruction.
Read the effective address from memory.
Execute the instruction.

## Slide 36: Instruction Cycle

## Slide 37: Instruction Cycle
Micro-operations for fetch & decode

## Slide 38: Basic Processing Unit

## Slide 39: Fundamental Concepts
Processor fetches one instruction at a time and perform the operation specified.
Instructions are fetched from successive memory locations until a branch or a jump instruction is encountered.
Processor keeps track of the address of the memory location containing the next instruction to be fetched using Program Counter (PC).
Instruction Register (IR)

## Slide 40: Executing an Instruction
Fetch the contents of the memory location pointed to by the PC. The contents of this location are loaded into the IR (fetch phase).
IR ← [[PC]]
Assuming that the memory is byte addressable, increment the contents of the PC by 4 (fetch phase).
PC ← [PC] + 4
(where each instruction comprises 4 bytes)
Carry out the actions specified by the instruction in the IR (execution phase).

## Slide 41: Processor Organization

## Slide 42
Registers:
The processor registers R0 to Rn-1 vary considerably from one processor to another.
Registers are provided for general purpose used by programmer.
Registers Y, Z & TEMP are temporary registers used by processor during the execution of some instruction.
Multiplexer:
Select either the output of the register Y or a constant value 4 to be provided as input A of the ALU.
Constant 4 is used by the processor to increment the contents of PC.

## Slide 43
ALU:
Used to perform arithmetic and logical operation.
Data Path:
The registers, ALU and interconnecting bus are collectively referred to as the data path.

## Slide 44: Register Transfers
B
A
Z
ALU
Y
in
Y
Z
in
Z
out
R
i
in
R
i
R
i
out
b
us
Internal processor
Constant 4
MUX
Figure 7.2. Input and output gating for the registers in Figure 7.1.
Select

## Slide 45
The input and output gates for register Ri are controlled by signals is Rin and Riout .
If Rin is set to1 - data available on common bus are loaded into Ri.
If Riout is set to1 - the contents of register are placed on the bus.
Riout is set to 0 – the bus can be used for transferring data from other registers .

## Slide 46: Data transfer between two registers:
Transfer the contents of R1 to R4.
Enable output of register R1 by setting R1out=1. This places the contents of R1 on the processor bus.
Enable input of register R4 by setting R4in=1. This loads the data from the processor bus into register R4.

## Slide 47: Performing an Arithmetic or Logic Operation
The ALU is a combinational circuit that has no internal storage.
ALU gets the two operands from MUX and bus. The result is temporarily stored in register Z.
What is the sequence of operations to add the contents of register R1 to those of R2 and store the result in R3?
  R1out, Yin
  R2out, Select Y, Add, Zin
  Zout, R3in

## Slide 48: Fetching a Word from Memory
Address into MAR; issue Read operation; data into MDR.
Figure 7.4. Connection and control signals for register MDR.

## Slide 49: Fetching a Word from Memory
The response time of each memory access varies (cache miss, memory-mapped I/O,…).
To accommodate this, the processor waits until it receives an indication that the requested operation has been completed (Memory-Function-Completed, MFC).
Example: Move (R1), R2
MAR ← [R1]
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory bus
R2 ← [MDR]

## Slide 50: Fetching a Word from Memory
Assume MAR is always available on the address lines of the memory bus.
Move (R1), R2
R1out, MARin, Read
MDRinE, WMFC
MDRout, R2in
Example: Move (R1), R2
MAR ← [R1]
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory bus
R2 ← [MDR]

## Slide 51: Storing a word in memory
Address is loaded into MAR
Data to be written loaded into MDR.
Write command is issued.
Example: Move R2,(R1)
R1out,MARin
R2out,MDRin,Write
  MDRoutE, WMFC

## Slide 52: Execution of a Complete Instruction
Example: Add (R3), R1
Fetch the instruction
Fetch the first operand (the contents of the memory location pointed to by R3)
Perform the addition
Load the result into R1

## Slide 53: Execution of a Complete Instruction
Add (R3), R1

## Slide 54: Question
Write the control sequence to execute
1. Add the (immediate) number NUM to register R1.
2. Add the contents of memory location NUM to register R1.
3. Add the contents of memory location whose address is at memory location NUM to register R1.

## Slide 55: Solution 1
PC out, MAR in, Read, Select4, Add , Zin
Zout, PCin, Yin, WMFC
MDRout, IR in,
IR NUMout , Yin
R1 out, Select Y, Add, Zin
Zout, R1in, End

## Slide 56: Solution 2
PC out, MAR in, Read, Select4, Add , Zin
Zout, PCin, Yin, WMFC
MDRout, IR in,
IRNUM out, MAR in, Read
R1out, Yin, WMFC
MDRout, Select Y, Add, Zin
Zout, R1in, End

## Slide 57: Solution 3
PC out, MAR in, Read, Select4, Add , Zin
Zout, PCin, Yin, WMFC
MDRout, IR in
IRNUM out, MAR in, Read
WMFC
MDRout, MAR in, Read
R1out, Yin, WMFC
MDRout , SelectY, Add, Zin
Zout, R1in, End

## Slide 58: Execution of Branch Instructions
A branch instruction replaces the contents of PC with the branch target address, which is usually obtained by adding an offset X given in the branch instruction.
The offset X is usually the difference between the branch target address and the address immediately following the branch instruction.
UnConditional branch

## Slide 59: Execution of Branch Instructions
Step
Action
1
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
2
Z
out
,
PC
in
,
Y
in
,
WMF
C
3
MDR
out
,
IR
in
4
Offset-field-of-IR
out
,
Add,
Z
in
5
Z
out
,
PC
in
,
End
Figure 7.7. Control sequence for an unconditional branch instruction.
Select Y
,

## Slide 60: Memory Organization
Memory Hierarchy
  Memory hierarchy in a computer system :
    Main Memory : memory unit that communicates directly with the CPU (RAM)
    Auxiliary Memory : device that provide backup storage (Disk Drives)
    Cache Memory : special very-high-speed memory to increase the processing speed (Cache RAM)

## Slide 61: Memory Organization
  Multiprogramming
    enable the CPU to process a number of independent program concurrently
  Memory Management System :
    supervise the flow of information between auxiliary memory and main memory
Memory Hierarchy is to obtain the highest possible access speed while minimizing the total cost of the memory system
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape

## Slide 62: Random Access Memory (RAM)
  RAM Chips
  Static RAM
  Consists of Flip-flops to store binary information.
  Static RAM is easier to use and having short Read/Write cycles
  Used mostly in Cache memory.
  Dynamic RAM
  Stores binary information in the form of electric charge stored inside the capacitor.
  The capacitors are provided by MOS transistors.
  Refreshing circuit is required to refresh the memory.
  Dynamic RAM offers reduced power consumption and large storage capacity.
  It is used to construct main memory.
    Typical RAM chip :
      128 X 8 RAM : 27 = 128 (7 bit address lines)
    Typical ROM chip:
      512 X 8 ROM : 29 = 512 (9 bit address lines

## Slide 63: Three State Buffer
2×4 Decoder
Select
Enable
0
1
2
3
S1
S0
E
A0
B0
C0
D0
Bus line with three-state buffer (replaces MUX0 in the previous diagram)
Output Y=A if C=1
High-impedence if C=0
Normal input A
Control input C

## Slide 64: MAIN MEMORY
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write
7-bit address
CS1
CS2
RD
WR
AD 7
128 x 8
RAM
8-bit data bus
CS1 CS2 RD WR
0 0 x x
0 1 x x
1 0 0 0
1 0 0 1
1 0 1 x
1 1 x x
Memory function
Inhibit
Inhibit
Inhibit
Write
Read
Inhibit
State of data bus
High-impedence
High-impedence
High-impedence
Input data to RAM
Output data from RAM
High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus
Main Memory

## Slide 65: MEMORY ADDRESS MAP
RAM 1
RAM 2
RAM 3
RAM 4
ROM
0000 - 007F
0080 - 00FF
0100 - 017F
0180 - 01FF
0200 - 03FF
Component
Hexadecimal
address
0 0 0 x x x x x x x
0 0 1 x x x x x x x
0 1 0 x x x x x x x
0 1 1 x x x x x x x
1 x x x x x x x x x
10 9 8 7 6 5 4 3 2 1
Address bus
Memory Connection to CPU
- RAM and ROM chips are connected to a CPU
through the data and address buses
- The low-order lines in the address bus select
the byte within the chips and other lines in the
address bus select a particular chip through
its chip select inputs
Address space assignment to each memory chip
Example: 512 bytes RAM and 512 bytes ROM
Main Memory

## Slide 66: CONNECTION OF MEMORY TO CPU
Main Memory
CS1
CS2
RD
WR
AD7
128 x 8
RAM 1
CS1
CS2
RD
WR
AD7
128 x 8
RAM 2
CS1
CS2
RD
WR
AD7
128 x 8
RAM 3
CS1
CS2
RD
WR
AD7
128 x 8
RAM 4
Decoder
3
2
1
0
WR
RD
9
8
7-1
10
16-11
Address bus
Data bus
CPU
CS1
CS2
512 x 8
ROM
AD9
1- 7
9
8
Data
Data
Data
Data
Data

## Slide 67: Numerical Problems
Q1. a) How many 128x8 RAM chips are needed to provide a memory capacity of 2048 bytes.
b) How any lines of the address bus must be used to access 2048 bytes of memory. How many of these lines will be common to all chips.
c) How many lines must be decoded for chip select? Specify the size of decoders.
Q2. Extend the memory system of Fig.1 to 4096 bytes of RAM and 4096 bytes of RAM. List the memory-address map and indicate what size decoders are needed.
Q3. A computer employs RAM chips of 256x8 and ROM chips of 1024x8. The computer system needs 2K bytes of RAM, 4K bytes of ROM, and four interface units each with four registers. A memory-mapped I/O configuration used. The two highest-order bits of the address bus are assigned 00 for RAM, 01 for ROM, and 10 for interface registers.
How many RAM and ROM chips are needed.
Draw a memory-address map for the system.
Give the address range in hexadecimal for RAM, ROM and interface.

## Slide 69: Cache Memory
Cache Memory
  Locality of Reference
    the references to memory tend to be confined within a few localized areas in memory
  Cache Memory : a fast small memory
    keeping the most frequently accessed instructions and data in the fast cache memory
  Hit Ratio
    the ratio of the number of hits divided by the total CPU references (hits + misses) to memory
      hit : the CPU finds the word in the cache
      miss : the word is not found in cache (CPU must read main memory)
  A computer with cache access time of 100ns, a main memory access time of 1000 ns, a hit ratio of 0.9 is having average access time of 200ns.

## Slide 70: Types of Mapping of Cache Memory
  Mapping
    The transformation of data from main memory to cache memory
      1) Associative mapping
      2) Direct mapping
      3) Set-associative mapping
  Associative Mapping:
    main memory : 32 K x 12 bit word (15 bit address lines)
    cache memory : 512 x 12 bit word
      CPU sends a 15-bit address to cache
        Hit : CPU accepts the 12-bit data from cache
        Miss : CPU reads the data from main memory (then data is written to cache)

## Slide 71: Associative Mapping

## Slide 72: Direct Mapping
  Direct mapping :
    n bit memory address
    Tag field (n - k) : Index field (k)
    2k words cache memory + 2n words main memory
        Tag = 6 bit (15 - 9), Index = 9 bit

## Slide 73: Direct Mapping
    Direct mapping cache with block size of 8 words :
      64 block x 8 word = 512 cache words size

## Slide 74: Set-Associative Mapping
  Set-associative mapping : (two-way)

## Slide 75: Questions
A two-way set associative cache memory uses blocks of four words. The cache can accommodate a total of 2048 words from main memory. The main memory size is 128Kx32. Formulate all pertinent information required to construct the cache memory. What is the size of cache memory.
A computer has a memory unit of 64Kx16 and a cache memory of 1K words. The cache uses direct mapping with a block size of four words. How many bits are there in the tag, index, block, and words fields of the address format. How many bits are there in each word of cache, and how are they divided into functions? Include a valid bit. How many blocks can the cache accommodate?
The access time of a cache memory is 100ns and that of main memory is 1000ns. It is estimated that 80 percent of the memory requests are for read and the remaining 20 percent for write. The hit ratio for read access only is 0.9. A write-through procedure is used. What is the average access time of the system considering only memory read cycles. What is the average access time of the system for both read and write requests. What is the hit ratio considering the write requests also.

## Slide 76: Answer

## Slide 77: Answer

## Slide 78
  Replacement Algorithm : cache miss or full
    1) LRU (Least Recently Used):
    2) Random Replacement:
    3) FIFO (First-In First-Out) :
  Writing to Cache :
      1) Write-through :
      2) Write-back :
  Cache Initialization
    Cache is initialized :
      1) When power is applied to the computer
      2) When main memory is loaded with a complete set of programs from auxiliary memory
      3) Cache is initialized by clearing all the valid bits to 0.
    Valid bit
      Indicate whether or not the word contains valid data

## Slide 79
VIRTUAL MEMORY
Give the programmer the illusion that the system has a very large memory,
even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
virtual address
(logical address)
physical address
address space
memory space
address generated by programs actual main memory address
Mapping
Virtual Memory

## Slide 80
VIRTUAL MEMORY
Address Mapping
Memory Mapping Table for Virtual Address -> Physical Address
Virtual address
Virtual
address
register
Memory
mapping
table
Memory table
buffer register
Main memory
address
register
Main
memory
Main memory
buffer register
Physical
Address
Virtual Memory

## Slide 81: ADDRESS MAPPING
Organization of memory Mapping Table in a paged system
Address Space and Memory Space are each divided
into fixed size group of words called blocks or pages
1K words group
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Block 3
Block 2
Block 1
Block 0
Address space
N = 8K = 213
Memory space
M = 4K = 212
0
000
1
001
1
010
0
011
0
100
1
101
1
110
0
111
1
Block 0
Block 1
Block 2
Block 3
MBR
0 1
0 1 0 1 0 1 0 0 1 1
1 0 1
0 1 0 1 0 1 0 0 1 1
Table
address
Presence
bit
Page no.
Offset
Virtual address
Main memory
address register
Memory page table
Main memory
11
00
01
10
01
Virtual Memory

## Slide 82: PAGE REPLACEMENT ALGORITHMS
FIFO
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
FIFO algorithm selects the page that has been in memory the longest time
Optimal Replacement (OPT) - Lowest page fault rate of all algorithms
Replace that page which will not be used for the longest period of time
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames
Reference string
Virtual Memory

## Slide 83: PAGE REPLACEMENT ALGORITHMS
- OPT is difficult to implement since it requires future knowledge
Replace that page which has not been
used for the longest period of time
LRU
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
Virtual Memory

## Slide 84: Question
The page request are in following order. If there are three memory frames, show the execution of the following pages using
a. FIFO b. Optimal c. LRU
6 0 1 3 2 5 0 4 7 1 3 2 6 0 4

## Slide 85: Input-Output Organization
Peripheral Devices: Input & Output devices attached to computer are called Peripheral.
Input and output devices communicate alphanumeric information by using ASCII 7bit code.
I/O interface provides a method for transferring information between internal storage and external I/O devices.
To use computer efficiently, large number of programs and data must be prepared in advance for execution with computer.
    .

## Slide 86: Input-Output Interface
The purpose of interfacing are as follows:
  Peripherals are electromechanical & electromagnetic devices and are interacting with electronics devices(CPU).
  Data transfer rate of peripherals is usually slower than transfer rate of CPU.
  Data codes and formats in peripherals differ from word format in CPU
  Operating modes of peripherals are different from each other and each one must be controlled without disturbing other.

## Slide 87: Input-Output Interface
To resolve these differences, computer system includes Interface units between CPU and peripherals to supervise and synchronize all input and output transfers.
Each peripheral has its own controller that operates a particular electromechanical device.
To communicate with a particular device, the processor places a device address on the address lines.

## Slide 88: Input-Output Interface

## Slide 89: Input-Output Interface
When the interface detects it own address, it activates path between bus lines and the device.
At the time address is made available in address lines, the processor provides function code(I/O command) in the control lines.
Types of I/O command:
Control command: To activate and inform what to do.
Status command: To test various status conditions.
Data Output data: It causes the transfer of data from bus into one of its registers.
Data Input Command: Interface receives data from peripheral and places them on buffer register where it is put into data lines.

## Slide 90: I/O versus Memory Bus
In addition to communicating to I/O, processor must also communicate with memory unit.
There are three ways that computer buses can be used to communicate with memory and I/O:
  Use two separate buses, one for memory and one for I/O. (IOP)
  Use one common bus for both memory and I/O but have separate control lines for each. (Isolated I/O)
  Use one common bus for memory and I/O with common control lines. (Memory Mapped I/O)

## Slide 91: Input-Output Transfer (IOP)
An IOP takes care of input and output tasks.
The CPU is assigned the task of initiating all operations, but I/O instructions are executed in IOP.
When an I/O operation is required, the CPU informs the IOP where to find the I/O program and then leaves the transfer details to the IOP.
IOP is also responsible of taking care of data synchronization, formats etc between CPU and I/O devices. In most computers CPU is master and IOP is slave.

## Slide 92: Input-Output Transfer (IOP)

## Slide 93: Isolated I/O
The distinction between memory and I/O transfer is made through separate read and control lines.
I/O read and I/O write are enabled during I/O transfer and Memory read/write are enabled during memory transfer.
In the isolated I/O configuration, CPU have distinct input and output instructions where each of it will be associated with address of the interface register.
When the CPU fetches and decodes the I/O instruction, it places the address associated with the instruction on the common address lines and enables I/O read or I/O write control line.

## Slide 94: Isolated I/O
When the CPU fetches and decodes the Memory instruction, it places the address associated with the instruction on the common address lines and enables Memory read or Memory write control line.
The isolated I/O method isolates memory and I/O addresses.

## Slide 95: Memory Mapped I/O
In this configuration, same address space is used for both memory and I/O.
The computer treats interface register (I/O) as a part of memory system.
The assigned address cannot be used for storing memory words, which reduces memory address range available.
In a memory-mapped I/O organization, there are no specific, input or output instruction.
CPU manipulate I/O data residing in interface registers with the same instruction used to manipulate memory words.

## Slide 96
Isolated I/O | Memory Mapped I/O
Memory and I/O have separate address space | Both have same address space
All address can be used by the memory | Due to addition of I/O addressable memory become less for memory
Separate instruction control read and write operation in I/O and Memory | Same instructions can control both I/O and Memory
In this I/O address are called ports. | Normal memory address are for both
More efficient due to separate buses | Lesser efficient
Larger in size due to more buses | Smaller in size
It is complex due to separate logic is used to control both. | Simpler logic is used as I/O is also treated as memory only.

## Slide 97: Memory Mapped I/O

## Slide 98: Modes of Transfer
Data transfer between the CPU and the I/O devices may be handled in variety of modes. Some modes use the CPU as an intermediate path and others transfer the data directly to and from the memory unit.
Data transfer to and from peripherals may be handled in three ways:
  Programmed I/O
  Interrupt-initiated I/O
  Direct Memory Access (DMA)

## Slide 99: Programmed I/O
Programmed I/O operations are the result of I/O instructions. Each data item transfer is initiate by an instruction in the program.
Usually the transfer is to and from a CPU register and peripheral. Other instructions are needed to transfer data between memory and CPU.
Once a data transfer is initiated, the CPU is required to monitor the interface to see when a transfer can again be made.

## Slide 100: Programmed I/O

## Slide 101: Interrupt Initiated I/O
In the programmed I/O CPU stays in program loop until the I/O indicates that it is ready for data transfer.
This is time consuming process since it makes CPU busy needlessly.
This can be avoided by using an interrupt facility.
When the interface determines that device is ready for data transfer, it generates an interrupt request.
Upon detecting external interrupt signal, the CPU momentarily stops the task it is processing.
It then branches to fulfill the I/O request and return to the original task.

## Slide 102: Direct Memory Access (DMA)
The transfer of data between a fast storage device such as magnetic disk and memory often limited to the speed of CPU.
Removing the CPU and letting the peripheral device manage the memory bus directly improve speed of transfer.
Such transfer technique is called Direct Memory Access (DMA).
A DMA controller takes over the buses to manage the transfer directly between I/O device and memory.
During DMA transfer, the CPU is idle and has no control over memory buses.
By using Bus Request(BR) and Bus Grant(BG) the buses are released to DMA controller.

## Slide 103: DMA
Data transfer ways:
  Burst Transfer: Here number of words are transferred in a block. Example: Magnetic disk.
  Cycle stealing: Allows the DMA controller to transfer one data word at a time after it must return the control of buses to CPU.

## Slide 104: DMA Controller

## Slide 105: Initialization of DMA
The CPU initializes the DMA by sending the following information through the data bus.
  The starting address of the memory block where data are available(for read) or where data are to be stored(for write).
  The word count, which is the number of words in the memory block.
  Control to specify the mode of transfer such as read or write.
  A control to start the DMA transfer.

## Slide 106: DMA Transfer in a computer system

## Slide 107: Bus Arbitration
The device that is allowed to initiate data transfers on the bus at any given time is called Bus master.
Bus arbitration is the process by which the next device becomes Bus master and will do the data transfer.
Two approaches: Centralized Arbitration and Distributed Arbitration.
        Centralized Arbitration

## Slide 108: Types of Interrupt
Major types of Interrupt are:
  External Interrupt: It comes from I/O devices, from timing device, or from any other external source.
  Internal Interrupt: It includes register overflow, invalid operation code, stack overflow etc.
  Software Interrupt or Hardware Interrupt: External and Internal interrupts are initiated from signals that occur in the hardware of the CPU. A software interrupt is initiated by executing an instruction.
  Priority Interrupt: In case several sources will request service simultaneously, in this case system must decide which device to service first. For ex: Polling, Daisy Chain.

## Slide 109: Buses
Data Bus: Bi-directional and transfers data.
Address Bus: Uni-directional and sends the address.
Control Bus: R/W, BR,BG etc.
Bus Structure: Single bus

## Slide 110: Buses
Bus Structure: Multi bus

## Slide 111: Synchronous or Asynchronous Data Transfer
Internal operations in a digital system are synchronized by means of clock pulses supplied by common pulse generator.
If the registers in the interface share a common clock with the CPU registers, the transfer is synchronous.
Asynchronous data transfer requires that control signals be transmitted between communicating units to indicate the time at which data is being transmitted.
Asynchronous data transfer can be accomplished by Strobe & Handshaking.

## Slide 112: Strobe Control
Strobe control:
  It employs single control line.
  It can be activated either by source or destination unit.

## Slide 113: Handshaking