## Slide 1: COMPUTER NETWORKS (BCSC 0008)
Copyright content, use only with the written permission of presenter mentioned
Lecture 2

## Slide 2: Analyzing components in N/W
Previously discussed components are
  Sender
  Receiver
  Message
  Medium
  Protocol

## Slide 3: Network Models
Network models use layers to describe networks
Each layer describes the services provided to the layer above it and those required from the layer below it
It also describes the format of exchanges between peer layers on different network hosts
Because the layers “stack” on top of one another, we often refer to network protocol “stacks” when we talk about the implementation
Layer N
Layer N+1
Layer N-1
Layer N+1
Layer N
Layer N-1
Provides
Requires
Exchanges
Building complex systems is hard!
  Approach: “Divide and conquer”.
  Split job into smaller jobs, or layers.
Each step dependent on the previous step but does not need to be aware of how the previous step was done.

## Slide 4
Analogy: Air Travel
The problem: air travel.
Decomposed into series of steps:
Arrival at airport
Check-in
Boarding
Takeoff
Departure from airport
Baggage claim (check out)
Deplane
Landing
Traveling

## Slide 5
Tasks involved in sending a letter ( Ref Fourouzan )
Task of communication broken up into modules

## Slide 6: Network Models
The most well-known network model is the OSI (Open Systems Interconnect) Reference Model defined and maintained by the Organization for International Standardization (ISO)
It consists of seven layers, numbered from the bottom (closest the network) to the top (closest the user)
Layer 1 – Physical
Layer 2 – Data Link
Layer 3 – Network
Layer 4 – Transport
Layer 5 – Session
Layer 6 – Presentation
Layer 7 – Application

## Slide 7
The interaction between layers in the OSI model

## Slide 8: Encapsulation/Decapsulation
At Sender Site, each layer add its own information to the data received from its upper layer ( Called as HEADER). ( HEADER + DATA= DATA for next lower layer)
This HEADER can be accessed (add/remove) only by specific layer
At Receiver Site, This HEADER is removed ( on matching certain conditions) only by the layer that has added the HEADER at sender site.

## Slide 9
Each Layer in OSI model provides different SERVICES

## Slide 10: OSI Reference Model
Layer 1 – The Physical Layer
  Defines the type of media to be used
  What order are bits transmitted (if serial or parallel)?
  Data Rate or Transmission Rate
  Line Configuration (P2P / MP)
  Physical Topology
  Transmission Mode ( Simplex, Half/ Full Duplex )
  Defines representation of data on the medium
    Is a ‘0’ “high” or “low”, “on” or “off”?
Layer 1 – Physical
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.

## Slide 11: OSI Reference Model
Layer 2 – The Data Link Layer
  Defines “right to transmit” rules (Access Control)
  Provides directly-connected hop-to-hop data transfer (Hop to Hop / Node to Node Delivery)
  Defines higher-level structure of data (frames)
  Defines “physical” address structure for hosts (Physical Addressing)
  Error Control
  Flow Control
Layer 1 – Physical
Layer 2 – Data Link
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 12: OSI Reference Model
Layer 3 – The Network Layer
  Provides end-host-to-end-host data transfer across multiple data links (host to host/ source to destination delivery)
  Defines higher-level structure of data (packets)
  Defines “abstract” address structure for host (Logical Addressing)
  Routing
  Delivery and Forwarding (Switching)
Layer 1 – Physical
Layer 2 – Data Link
Layer 3 – Network
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 13
Figure 2.9 Source-to-destination delivery
Data Link Layer- Hop to Hop
Network Layer- Source to Destination

## Slide 14: OSI Reference Model
Layer 4 – The Transport Layer
  Provides process-to-process data transfer
  May provide for reliable data transfer
  Defines higher-level structure for data (datagrams, streams, etc.)
  Defines “port” addresses for services (processes)
Layer 1 – Physical
Layer 2 – Data Link
Layer 3 – Network
Layer 4 – Transport
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 15
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 16: OSI Reference Model
Layer 5 – The Session Layer
  Provides a logically persistent connection between processes
  May involve user or host authentication (login), transaction encapsulation (for database access), etc.
Layer 1 – Physical
Layer 2 – Data Link
Layer 3 – Network
Layer 4 – Transport
Layer 5 – Session
The session layer is responsible for dialog control and synchronization.

## Slide 17: OSI Reference Model
Layer 6 – The Presentation Layer
  Defines the network representation of data
  Converts between the network and host representations of data (ASCII/EBCDIC, byte order, encryption, compression, etc.)
Layer 1 – Physical
Layer 2 – Data Link
Layer 3 – Network
Layer 4 – Transport
Layer 5 – Session
Layer 6 – Presentation
The presentation layer is responsible for translation, compression, and encryption.

## Slide 18: OSI Reference Model
Layer 7 – The Application Layer
  Provides a portal for the application to access the network
  Describes the dialog between two applications communicating across the network.
Layer 1 – Physical
Layer 2 – Data Link
Layer 3 – Network
Layer 4 – Transport
Layer 5 – Session
Layer 6 – Presentation
Layer 7 – Application
The application layer is responsible for providing services to the user.

## Slide 19
Summary of OSI Layers

## Slide 20
Thank You
Discussion & Doubt session will be in lecture.
Important terms to keep in mind
  Network Model
  Encapsulation / Decapsulation
  Peer to Peer process
  OSI model and services of layers