## Slide 1: Digital Data Transmission

## Slide 3: Parallel Transmission
Multiple bit can be sent at one clock tick
To send 8 bits, 8 separate lines are required
Advantages:
High Speed
Disadvantages:
Cost
Limited to shorted distance

## Slide 4: Serial Transmission

## Slide 5: Asynchronous Serial Transmission
Time is not important
Send every byte with start and stop bit
0 start bit. Alerting receiver that data is coming
1 stop bit, indicating end of byte
Gap is variable. Variable interval between data units

## Slide 6: Applications:
Low speed transmission of narrow band
Slow speed voice channel
Manual operated devices
Low speed communication where gap occur like keyboard

## Slide 7: Advantages and Disadvantages
Advantages
Very cheap (less costly)
Effective
Disadvantages
Slow
Additional overhead of start and stop bit

## Slide 8: Synchronous Serial Transmission
Time is important
High speed data transmission
Multiple bytes send together
Receiver receive data continuously until detect special ending character
No gaps
Perform error detection using CRC

## Slide 9
Advantages:
High speed
No gap
No overhead
Disadvantage:
Real time transmission cannot be possible
Applications:
Fast voice and broadband channel
Computer to computer communication

## Slide 10: Isochronous Serial Transmission

## Slide 11
Application:
High rate of transmission than asynchronous
Real time audio and video and TV