## Slide 1: Error Detection and Correction
Types of Errors
Detection
Correction

## Slide 2
Basic concepts
Networks must be able to transfer data from one device to another with complete accuracy.
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 3
Types of Errors

## Slide 4
Single-bit error

## Slide 5
Single bit errors are the least likely type of errors in serial data transmission because the noise must have a very short duration which is very rare. However this kind of errors can happen in parallel transmission.
Example:
If data is sent at 1Mbps then each bit lasts only 1/1,000,000 sec. or 1 μs.
For a single-bit error to occur, the noise must have a duration of only 1 μs, which is very rare.

## Slide 6
Burst error

## Slide 8
The term burst error means that two or more bits in the data unit have changed from 1 to 0 or from 0 to 1.
Burst errors does not necessarily mean that the errors occur in consecutive bits, the length of the burst is measured from the first corrupted bit to the last corrupted bit. Some bits in between may not have been corrupted.

## Slide 9
Burst error is most likely to happen in serial transmission since the duration of noise is normally longer than the duration of a bit.
The number of bits affected depends on the data rate and duration of noise.
Example:
If data is sent at rate = 1Kbps then a noise of 1/100 sec can affect 10 bits.(1/100*1000)
If same data is sent at rate = 1Mbps then a noise of 1/100 sec can affect 10,000 bits.(1/100*106)

## Slide 10: Error detection
Error detection means to decide whether the received data is correct or not without having a copy of the original message.
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.
Notes: Make sense of message.
Make sense of message.

## Slide 11
Redundancy

## Slide 12
Four types of redundancy checks are used
in data communications

## Slide 13
Vertical Redundancy Check
VRC

## Slide 14: Performance
It can detect single bit error
It can detect burst errors only if the total number of errors is odd.

## Slide 15
Longitudinal Redundancy Check
LRC

## Slide 16
Performance
LCR increases the likelihood of detecting burst errors.
If two bits in one data units are damaged and two bits in exactly the same positions in another data unit are also damaged, the LRC checker will not detect an error.

## Slide 17
VRC and LRC

## Slide 18
Cyclic Redundancy Check
CRC

## Slide 19: Cyclic Redundancy Check
Given a k-bit frame or message, the transmitter generates an n-bit sequence, known as a frame check sequence (FCS), so that the resulting frame, consisting of (k+n) bits, is exactly divisible by some predetermined number.
The receiver then divides the incoming frame by the same number and, if there is no remainder, assumes that there was no error.

## Slide 20
Binary Division

## Slide 21
Polynomial

## Slide 22
Polynomial and Divisor

## Slide 23
Standard Polynomials

## Slide 24
Checksum

## Slide 25: At the sender
The unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented and becomes the checksum.
The checksum is sent with the data

## Slide 26: At the receiver
The unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented.
If the result is zero, the data are accepted: otherwise, they are rejected.

## Slide 27: Performance
The checksum detects all errors involving an odd number of bits.
It detects most errors involving an even number of bits.
If one or more bits of a segment are damaged and the corresponding bit or bits of opposite value in a second segment are also damaged, the sums of those columns will not change and the receiver will not detect a problem.

## Slide 28: Error Correction
It can be handled in two ways:
receiver can have the sender retransmit the entire data unit.
The receiver can use an error-correcting code, which automatically corrects certain errors.

## Slide 29: Single-bit error correction
To correct an error, the receiver reverses the value of the altered bit. To do so, it must know which bit is in error.
Number of redundancy bits needed
Let data bits = m
Redundancy bits = r
Total message sent = m+r
The value of r must satisfy the following relation:
2r ≥ m+r+1

## Slide 30
Error Correction

## Slide 31
Figure 10.12 The structure of the encoder and decoder for a Hamming code

## Slide 32: Hamming Code
Parity checks are created as follow (using modulo-2)
  r0 = a2 + a1 + a0
  r1 = a3 + a2 + a1
  r2 = a1 + a0 + a3

## Slide 33: Hamming Code
The checker in the decoder creates a 3-bit syndrome (s2s1s0).
In which each bit is the parity check for 4 out of the 7 bits in the received codeword:
s0 = b2 + b1 + b0 + q0
s1 = b3 + b2 + b1 + q1
s2 = b1 + b0 + b3 + q2
The equations used by the checker are the same as those used by the generator with the parity-check bits added to the right-hand side of the equation.

## Slide 34: Example of Hamming Code for message length 4
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format

## Slide 35: Which bit is flipped?
For message of length 4 bits:
Where
Parity-check matrix for the above code:
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format
7 | 6 | 5 | 4 | 3 | 2 | 1 | Position
 |  |  |  |  |  |  | Code group format

## Slide 36
Table 10.5 Logical decision made by the correction logic analyzer
Hamming code C(7, 4) can :
detect up to 2-bit error (dmin -1)
can correct up to 1 bit error (dmin-1)/2